## Slide 1
DSP Pipeline
GSM Channel Scan Engine
Sampige Semiconductor R&D · Internship project
gsm_dataset_gen.py
fft_channeliser.py
pfb_channeliser.py
3 Python files · numpy + scipy only

## Slide 2
01 PROBLEM
What are we scanning?
104 MS/s
ADC sample rate
25 channels
200 kHz each
5-bit I/Q
Signed integers
Goal: decide for each of the 25 channels whether a GSM carrier is present
Output: 25-element binary occupancy vector — 1 = occupied, 0 = empty

## Slide 3
02 DATASET GENERATOR
gsm_dataset_gen.py
SELF-CONTAINED
Generates synthetic 5-bit IQ windows at 104 MS/s with labelled GSM carriers and impairments.
①
GMSK modulator
Gaussian-filtered CPM, BT=0.3, SPS=4 — no external GSM library
②
GSM burst builder
FCCH / SCH / BCCH / CCCH 51-multiframe — Fire code + conv encoder R=1/2 K=5
③
Frequency placement
683 native samples → FFT-resample → freq-shift to slot centre at 104 MS/s
④
Impairment injection
6 binary flags: CFO, static fading, time-varying fading, CW tone, adjacent channel, blocker
⑤
Labels per sample
occupancy (25,) · power_class (25,) · impairment_flags (6,) · snr_db · cfo_hz

## Slide 4
02 DATASET GENERATOR — COMMANDS
gsm_dataset_gen.py — how to run
Install
pip install numpy scipy
Generate 1000 samples
python gsm_dataset_gen.py --n-samples 1000 --out-dir ./gsm_dataset --seed 42
Scale up / resume
# Stage 1 — sanity check
python gsm_dataset_gen.py --n-samples 50000 --out-dir ./stage1
# Resume from sample 4700
python gsm_dataset_gen.py --n-samples 50000 --start-idx 4700 --seed 42
Load a sample in Python
d = np.load('sample_0000042.npy', allow_pickle=True).item()
iq = d['iq'] # (2, 65536) int8
occ = d['occupancy'] # (25,) uint8 — ground truth

## Slide 5
03 FFT CHANNELISER
fft_channeliser.py
DSP BASELINE
Textbook 7-step FFT energy detector. Splits 5 MHz into 25 channels and decides occupancy from energy alone.
1
form_complex()
x[n] = I[n] + j·Q[n] from (2, 65536) int8 input
2
decimate()
FFT-resample 104 MS/s → 5 MS/s (65536 → 3151 samples, same 630 µs)
3
apply_window()
Hann window — tapers edges to 0, suppresses inter-channel spectral leakage
4
compute_fft()
1024-pt FFT + fftshift → power spectrum, 4882 Hz/bin, Parseval-normalised
5
channel_power()
Sum 41 bins per channel (bins [k×41 : k×41+41]) → 25 energy values
6
noise_floor()
Median of 25 channel energies — robust to up to 12 occupied channels
7
threshold_decision()
Occupied if energy > k × noise_floor (sweep k for ROC curve)

## Slide 6
03 FFT CHANNELISER — COMMANDS
fft_channeliser.py — how to run
Basic evaluation on a dataset
python fft_channeliser.py --dataset ./gsm_dataset
With P_d vs SNR table
python fft_channeliser.py --dataset ./gsm_dataset --pd-snr
ROC curve — sweep threshold from 0.5× to 30×
python fft_channeliser.py --dataset ./gsm_dataset --roc
Step-by-step output on one sample
python fft_channeliser.py --sample ./gsm_dataset/samples/sample_0000042.npy
Change threshold multiplier
python fft_channeliser.py --dataset ./gsm_dataset --threshold 2.0 --pd-snr

## Slide 7
04 PFB CHANNELISER
pfb_channeliser.py
DSP BASELINE
Polyphase Filter Bank channeliser. Proper per-channel filtering via prototype lowpass filter decomposed into N polyphase branches.
1+2
prepare_signal()
Form complex x[n] = I[n] + j·Q[n], then FFT-resample to 5 MS/s
3+4
design_prototype_filter()
polyphase_decompose()
Kaiser-windowed sinc, 400 taps → polyphase matrix G of shape (25, 16)
5
pfb_process()
Per block: input matrix X (25×16) · branch filter G → v[p] → FFT+fftshift → y_k
6
noise_floor()
Median of 25 channel powers — same CFAR approach as FFT channeliser
7+8
threshold_decision()
Occupied if power > k × noise_floor
Key parameters: N=25 channels · L=16 taps per branch · 400-tap prototype filter · ~40 dB channel isolation

## Slide 8
04 PFB CHANNELISER — COMMANDS
pfb_channeliser.py — how to run
Basic evaluation
python pfb_channeliser.py --dataset ./gsm_dataset
P_d vs SNR + ROC curve
python pfb_channeliser.py --dataset ./gsm_dataset --pd-snr --roc
Step-by-step output — shows filter details and per-channel decisions
python pfb_channeliser.py --sample ./gsm_dataset/samples/sample_0000042.npy
Print prototype filter design details
python pfb_channeliser.py --filter-info
Limit to first 500 samples (faster for quick checks)
python pfb_channeliser.py --dataset ./gsm_dataset --n-samples 500 --pd-snr

## Slide 9
05 RESULTS
Detector performance summary
Detector
P_d
P_fa
F1
Notes
FFT Channeliser
0.333
0.011
0.467
k=3.0×, median CFAR
PFB Channeliser
0.056
0.045
0.078
Short 630 µs window
ML model target
≥ 0.90
≤ 0.05
≥ 0.85
Uses spectral shape
Why is PFB worse?
The PFB divides the 3151-sample window into 126 blocks of 25 samples each. Each block is only 5 µs. Averaging 126 noisy power estimates over such short slices gives a weaker result than one FFT over the full 630 µs window.
Energy detectors cannot detect signals below 0 dB SNR. The ML model must exploit spectral shape, envelope variance, and temporal features to close P_d from 0.33 to ≥ 0.90.